## Slide 1
Solving Three-Phase Distribution OPF
with Nonlinear Programming
Frederik Geth, François Pacaud, Rahmat Heidari
University of Queensland · Mines Paris-PSL
128
LV Networks
3
Formulations
2
NLP Solvers
PSCC 2026 · Limassol, Cyprus · June 2026

## Slide 2
Why Is Distribution OPF Different?
Transmission OPF
Single-phase (positive sequence)
Power-polar voltage (SVP) formulation is best
Interior point method converges easily
Sparse, well-conditioned Jacobian
Distribution OPF
Three-phase with 3×3 impedances (not diagonalizable in general), no grounded terminals
Unbalanced loads + untransposed lines
Mutual coupling between phases means less sparse system of equations
3× more variables → new challenges
Key question: which nonlinear formulation works best for distribution networks, up to 3-wire?

## Slide 3
Three Distribution OPF Formulations Under Study
IVR
Current–Voltage
Rectangular
Quadratic constraints
No automatic differentiation overhead
Most variables (n=1758)
Near-singular Hessian (κ≈10¹⁴)
SVR
Power–Voltage
Rectangular
Quadratic constraints
No automatic differentiation overhead
Fewer variables (n=1062)
Well-conditioned (κ≈10⁷)
SVP
Power–Voltage
Polar
Trig functions (sin/cos/tan)
Heavy automatic differentiation overhead
Fewer variables (n=1062)
Well-conditioned (κ≈10⁷)
Transmission consensus: power-polar-voltage is best. What about distribution?

## Slide 4
Practical Pitfalls: What Can Go Wrong
⚠
Wrong Phase Initialization
Zero or negative-sequence start causes high failure rates. Always use positive-sequence: 1∠0°, 1∠−120°, 1∠+120°
⚠
Power Base Too Large
Transmission standard (100 MVA) causes numerical inaccuracy. Use ≤1000 kW for distribution networks.
⚠
Degenerate Angle Reference
Without a voltage angle reference, all angles can shift freely — the problem becomes degenerate.
✓
Add Angle Difference Constraints
Constrain inter-phase angles near ±120°. Improves robustness with no significant runtime cost.
✓
Merge Degree-2 Buses
Superfluous pass-through buses inflate problem size. Merging branches in series speeds up solution.
✓
Add Realistic Current Limits
Missing current bounds widen the feasible set. Add limits correlated with conductor cross-section.

## Slide 5
Benchmark data set: 128 LV Networks from UK (ENWL)
Dataset & Setup
128 single-grounded UK LV network models
All three-phase lines, single-phase loads
Realistic current limits added
Degree-2 buses eliminated
Dispatchable generators with linear cost
Julia 1.11 + JuMP / ExaModels
IPOPT 3.14 + HSL MA27
KNITRO 15.0 for comparison
Options Tested
Formulations:
IVR, SVR, SVP
Voltage source:
3vm3vafix, 3vafix, vafix, vafixvadiff, vafixseq
Angle init:
pos, neg, zero
Sequence bounds:
on / off
Angle diff bounds:
on / off
Power base:
10 → 1,000,000 kW
V. Rigoni, L. F. Ochoa, G. Chicco, A. Navarro-Espinosa and T. Gozel, "Representative Residential LV Feeders: A Case Study for the North West of England," in IEEE Transactions on Power Systems, vol. 31, no. 1, pp. 348-360, Jan. 2016, doi: 10.1109/TPWRS.2015.2403252.

## Slide 6
Main Result: Best Formulation Depends on Solver
Chart: Total time (s) — 128 instances
| IVR | SVR | SVP (JuMP) | SVP (ExaModels)
IPOPT | 24.8 | 56.2 | 128.2 | 65
KNITRO | 56.3 | 22.1 | 73.9 | 32.5
IPOPT → IVR wins
24.8s total
Filter line-search handles IVR well despite near-singular Hessian
KNITRO → SVR wins
22.1s total
Trust-region algorithm avoids IVR degeneracy, SVR wins
Power polar voltage is slowest for both solvers — contrary to transmission OPF!

## Slide 7
Why Is SVP Slower in Distribution?
01
Automatic Differentiation Overhead
Power polar voltage uses sin, cos, tan — requires automatic differentiation to compute derivatives. With 3× more constraints than single-phase OPF, automatic differentiation cost dominates.
02
Harder Newton Linear Systems
The 3-phase model makes Newton systems denser and harder to factor. More time per iteration in the sparse linear solver.
03
ExaModels Helps — But Not Enough
Replacing JuMP with ExaModels halves power-polar voltage time (128s → 65s with IPOPT). Still 2.6× slower than IVR.
04
IVR & SVR Are Automatic Differentiation-Free
Quadratic formulations: derivatives are computed analytically. No automatic differentiation bottleneck, lower overhead per iteration.
Bottom line: 3-phase complexity punishes SVP more than IVR/SVR

## Slide 8
Numerical Scaling: Choose Your Power Base Carefully
✓ Safe zone
sbase ≤ 1000 MVA
Negligible numerical error
✗ Danger zone
sbase = 100 MVA
Transmission standard → avoidable inaccuracy in distribution!
The per-unit power base is a modeler's choice — make it ≤ 1000 MVA for these LV distribution feeders.

## Slide 9
Practical Guide: Do's and Don'ts
✓ DO
Use IVR with IPOPT, SVR with KNITRO
Set power base ≤ 1000 kW (never 100 MVA)
Fix at least one voltage angle reference
Add inter-phase angle difference constraints
Merge degree-2 buses before solving
Add realistic branch current limits
Use positive-sequence initialization: 1∠0°, 1∠−120°, 1∠+120°
✗ DON'T
Assume SVP is best (it's not — unlike in transmission)
Use 100 MVA as power base for distribution
Omit voltage angle reference (problem degenerates)
Use KNITRO expecting IVR to be fastest
Leave redundant data in the network model
Forget current limits (inflates feasible set)
Use zero or negative-sequence initialization

## Slide 10
Conclusions
→
IVR is fastest with IPOPT; SVR is fastest with KNITRO. SVP is slowest for both — opposite of transmission OPF.
→
Initialization matters: always use positive-sequence. Zero/negative sequence causes failures.
→
Power base must be ≤ 1000 kW. The 100 MVA transmission standard causes numerical inaccuracy.
→
Angle difference constraints improve robustness at negligible computational cost.
→
Data preprocessing (merging buses, adding limits) is essential for a well-posed problem, needs more efforts.
Future: GPU acceleration · SDP relaxations · Multiperiod OPF
github.com/hei06j/PMDlab.jl